1a) 3.3708567 x 10-19 J

b) 5.9332098 x 1020 photons

2a) 7.4245799 x 10-19

b) 4.6340583 eV

3) 3.38945138 m/s

4) Consider a blackbody radiator at temperature T. We know the energy density, {E_total( T ) } over V, is given by
int from 0 to infinity { %rho(%nu,T)d%nu } = int from 0 to infinity {{ {8%pi h%nu^3} } over {c^3(e^{{h%nu} over {k_{B}T}})-1}}d%nu . Let x = {{h%nu} over {k_{B}T}}, then we have dx = {{h} over {k_{B}T}}d%nu drarrow d%nu = {k_{B}T} over {h} dx and then x^3 = ({{h} over {k_{B}T}})^3 %nu^3 drarrow %nu^3 =( {{h} over {k_{B}T}} )^3 x^3 . Substituting these formulae into the original equation we arrive at
{{E_total( T ) } over V} = {{{ 8%pi h } over { c^3 }} {int from 0 to infinity { {{k_B}^{3}T^{3}h^{-3}{x^3}} over {e^x -1} } }(k_B Th^-1)dx} = {8%pi{ k_{B} }^4{ T^4}} over { (hc)^3 } int from 0 to infinity { x^3 over {e^x -1} } dx = ({8%pi{ k_{B} }^4{ T^4}} over { (hc)^3 }) ({%pi^4} over {15}) = %sigma T^4 where
%sigma = (8 over 15) { %pi^5 {k_b}^4 } over { (hc)^3 } is a constant. Therefore the energy depends on temperature as T4.

5a) 5.2728591 x 10-26 J

b) 3.17538996 x10-2 J·mol-1

6a) 6329.9109 Å

b) 15798.011 cm-1

c) 299709770 m/s

7a) For X-Rays of wavelength 3.00 x 10-10 m (3.00 Å) incident at an angle of 90° = %pi over 2 radians the change in wavelength is described by the equation {%DELTA}{ %lambda } = {( 1-cos%theta )h} over {{m_e}c} = {( 1-cos( {%pi} over 2) )h} over {{m_e}c} = {h} over {{m_e}c} = 2.4263102x10^{-12} m so the final wavelength of the scattered X-Rays is %lambda_final = %lambda_intial +{ %DELTA }%lambda=3.0242631 x 10^-10 m.

b) The initial energy of the incoming X-Ray photon is given by E=h%nu={ hc }over{ %lambda }= 6.6214862x10^{-16}J, by the same relation we know that the final energy of the scattered photon is 6.5683632x10^{-16}J and because energy is conserved (even if momentum is not because this is an inelastic collision) we know that the energy lost by the scattered X-Ray photon will be equal to the kinetic energy gained by the scattered electron. Thus we have KE_electron = %DELTA E_photon = E_f - E_i=5.3122957x10^{-18}J = 1 over 2 m_electron v^2 drarrow v=sqrt{ {2(KE_electron)} over m_electron } which is equal to 3.41516443x10^6 m over s.

8a)